## Slide 1: Kenya Medical Training College
Department:Cotm
Subject :Material science
Year :One
Semester : One
Class : March 2020
Facilitator : Nancy Chesire

## Slide 2: Learning outcomes:
By the end of this lesson, you should be able to:
Classify materials used in management of orthopaedic and trauma conditions
Demonstrate understanding of properties of materials used in management of orthopaedic and trauma patients
Identify tools used in orthopaedic and trauma management
Identify equipment used in management of orthopaedic and trauma condition

## Slide 3: Definition
The scientific study of the properties and applications of materials of construction or manufacture (such as ceramics, metals, polymers and composites
OR
An interdisciplinary field concerned with understanding and application of properties of matter. Scientists study the connections between the underlying structure of a material, its properties, its processing methods and its performance in application

## Slide 4: Importance of material science
It involves applications from number scientific disciplines that contribute to the creation of new materials. Chemists play a predominant role in materials science because chemistry provides information about the structure and composition of materials as well as the processes to synthesize and use them

## Slide 5: Historical background of materials
Tools allowed hominids to become the masters of their environment, to hunt, to build and to perform important tasks that made life easier for them. The first tools were made out of stone. Thus, the historians refer to the period of time before written history as stone age
Copper is one of those metals that man started using very early. As a matter of fact, copper was the fist metal that man discovered in 9000 BCE. The other metals used in the pre-historic times were gold, silver, tin, lead and iron.

## Slide 6: Terminologies
Alloy- A harmonious mixture of two or more metals made up of distinct components or elements
Annealing- To heat (glass or metal) and slowly cool it to toughen and reduce brittleness
- To temper
Atom- A unit of matter, the smallest unit of an element, having all the characteristics of that element and consisting of a dense, positively charged nucleus surrounded by a system of electrons

## Slide 7: Cont.,
Carbon- A non metallic chemical element found especially in all organic compounds, diamond and graphite are pure carbon
Carbonaceous- Man- made fibers. Created using heat
Catalyst- A substance serving as the agent in the speeding up or sometimes slowing down of a chemical reaction by adding a substance which itself is not changed thereby

## Slide 8: Cont.,
Compound- A substance consisting of atoms or ions of two or more different elements in definite proportions, usually having properties unlike those of its constituent elements
Density- A comparison of the relative weights of materials. The ratio of mass to unit volume expressed in grams/cm3 for solids and liquids and grams/litre in glass(density= mass/volume
Ductility- The ability of a material to be stretched and or compressed without fracture

## Slide 9: Cont.,
Durometer- Technically, this term refers to the hardness of a material and ranges from a skin soft OA to a harder than a car tire 95A. There are different scales used to determine a materials hardness that we should be aware of (read more on other scales)
Elasticity- The ability of a material to recover its original shape after deformation
Element- A substance composed of atoms having identical number of protons in each nucleus and not reducible to a simpler substance

## Slide 10: Cont.,
Fatigue resistance- The ability of a material to withstand cyclic loading with limited failure
Ferrous- of , containing, or derived from iron (a metallic chemical element, the most common of all metals
Fiber- A thread like structure that combines with others to form animal or vegetable tissue
- Any substance that can be separated into threadlike parts for weaving

## Slide 11: Cont.,
Texture
Character or nature
Roughage
Graphite- Crystalline form of carbon used in pencils such as lubricant and formed into man made fibers etc.
Melting point-The temperature at which a solid becomes liquid at standard atmospheric pressure
Monometer- A substance composed of molecules capable of reacting with like or unlike molecules to form polymers. Any small molecule that can undergo a

## Slide 12: Cont.,
reaction in which it is incorporated into a large molecule containing many similar units.
Common monomers are vinyl acetate, styrene, butadiene and vinyl chloride (it is appropriate to consider hydrocarbons as polymers of methylene)
Non ferrous of or containing no iron
Polymer- Substance composed of molecules characterized by the repletion (neglecting ends, branch junctions and other minor irregularities) of one or more types of monomeric units

## Slide 13: Cont.,
Polymerization- The process in which many small molecules (molecular weight are joined together to form a few, much larger molecules. The two ways in which this happens are chain growth and step growth polymerization
Plasticity- The ability of a material to be formed to a new shape without fracture and retain that shape after load removal
Plasticizer- A compound added to a polymer to make it softer and more flexible. These are usually small molecules with dangling bits that can disrupt the packing of polymer chains

## Slide 14: Cont.,
Strain- A materials reaction to a stress
Strength- The ability to withstand load, to resist an applied force without failure
Stress- The reference to the force being applied
Stress relieved- This term is used to indicate that a specific process was used to align the molecules of a material in their most efficient configuration
Substance- That which has mass and occupies space, matter - A material of a particular kind of constitution

## Slide 15: Cont.,
Tensile strength- The word tensile is to pull apart. Tensile strength is the resistance of material to being pulled apart and is expressed in lbs. per square inch. The maximum tensile load per unit area of original cross section, within the gage boundaries, sustained by the specimen during a tension test. It is expressed as PSI. Tensile load is interpreted to mean the maximum tensile load sustained by the specimen during the test, whether or not this coincides with the tensile load at the moment of rupture

## Slide 16: Cont.,
Tensile modulus- When a bar is pulled in tension, it has to get longer. The tensile modulus is used to calculate how much longer it will get when a certain load is applied to it. Units are normally millions of pounds per square inch. (106 PSI)-Giga Pascal's (gpa)
- Higher numbers indicate materials which will not elongate as much as others when they are being compared under equal tensile loading conditions

## Slide 17: Cont.,
Thermoforming- This is a term used to describe several techniques for making products from plastic sheets. In a vacuum forming process, hot thermoplastic sheets are draped over a mold. Removing air from between the mold and the plastic creates a vacuum that draws the plastic to the surface of the mold

## Slide 18: Cont.,
Thermoset- A polymer that when heated (thermo) does not become soft and deformable. This usually because it is cross-linked, and the molecules comprising it cannot move past one another unless chemical bonds are actually broken which leads to the decomposition of the polymer. Phenol-formaldegyde resin is an example

## Slide 19: Cont.,
Thermosets- Reference to the make-up of monomers that when formulated in a liquid state solidifies by chemical reaction. Because of the chemical reaction, the material is often not adjustable once the mixture has set

## Slide 20: Cont.,
Thermoplastics- Reference to the make up of monomers that when formulated in a liquid state solidifies by cooling. In particular the materials capability to be melted repeatedly. A polymer that when heated (thermo) becomes soft and deformable(plastic) examples are poly(styrene)and poly(ethylene)

## Slide 21: Cont.,
Toughness- The ability of a material to withstand sudden or shock loading forces without fracture
Viscosity- This term indicates how well a material does or does not flow and is measured in centipoise (CPS). Water has a viscosity of 1CPS and flows easily. Molasses has a viscosity of 100,000 cps and is very thick resulting in a much slower flow rate

## Slide 22: Cont.,
Volume resistivity- The property of a material to resist electric conductivity

## Slide 23: Material science
Are items used to handle trauma patients
It requires a lot of chemicals
Equipment used CT scans, MRI and x-rays

## Slide 24: Importance of material science
It equips the learner on how to customize materials that use to fit trauma patients
Gives guidance to the learner on choosing materials
Equips the student on the technology of materials essential for a given task
Gives guidance on choosing the materials

## Slide 25: Materials used
Leather material
Wood material
Metallic material
Ceramic material
Rubber material
Adhesive materials
Plastic materials
Fabric materials

## Slide 26: Plaster of Paris
Definition- A quick- setting gypsum plaster consisting of a fine white powder (calcium sulphate hydrate) which hardens when moistened and allowed to dry
Known since ancient times and it is prepared from gypsum found near Paris
Chemical formula (Caso4)

## Slide 27: Characteristics
Soaks rapidly
Smooth when molding
Creamy
Light and translucent to x-rays
Cost effective affordable
durable

## Slide 28: Advantages
Offers arid protection
Easy to apply
Show of low allergic response
Sees better than synthetic
Disadvantages:
Causes circulatory impairment
Causes pressure sores
Causes stiffness to joints

## Slide 29: Cont.,
Loss of position of the fracture of the trauma patient
It is not water proof
Uses:

## Slide 30: Fabrics
Definition: Cloth or other materials produced by weaving together cotton, nylon, wool, silk or other threads
Uses: They are used for making things such as clothes, curtains and sheets

## Slide 31: Properties of fabrics
Breathability
Weight
Drape
Durability
Softness
Water repellant

## Slide 32: Fiber glass
Common type of fiber- reinforced plastic using glass fiber. The fibers may be randomly arranged, flattened into a sheet (called a chopped stand mat) or woven into a fabric
Uses:
Boat building
Vehicle bodies
Architectural components

## Slide 33: How it is made
Manufactured primarily from borosilicate glass by drawing the molten glass into fibers
Properties of fiberglass fabrics:
Chemical resistance- Fiber glass textile fabrics will not mildew or deteriorate
Dimensional stability- fiber glass fabrics will stretch or shrink
Good thermal properties
High thermal endurance

## Slide 34: Cont.,
Low moisture absorption
Electrical insulation
Product versatility

## Slide 35: Fasteners and Adhesives
Definition- Are substances that are capable of holding materials together in a functional manner that resist separation
Examples:
Cement
Glue
paste

## Slide 36: Types of adhesives
Chemical adhesives
Load capacity adhesive
Structural adhesive
Pressure sensitive adhesive
Characteristics of adhesives:
Pressure sensitive
Rigid and creep resistance
strong

## Slide 37: Uses
To connect the parts of toys
Sticking envelopes
Joining any broken material
Assembling any spare parts

## Slide 38: Rubber
Materials which can stretch or shrink
Types:
Natural
Butyl
Synthetic
silicon

## Slide 39: Characteristics
Resiliency
Elongation strength
Tear resistance
Tensile resistance
Uses:
Making tires and tire tubes
Used in belt
Making of horse pipes

## Slide 40: Cont.,
Medical gloves
Plastics: Puffy like substances which are capable to be molded or framed
Properties of plastics:
Easy to fabricate
Have a good appearance
Resistances to body fluids
Relatively light
Posses good mechanical strength

## Slide 41: Cont.,
Have adaptability to fabrication technique
Have a wide variety of colors
Flexible
Durable

## Slide 42: Properties compared to other material metals
Are weak if not fabricated
Good electrical and thermal insulators
Most are resistant to corrosion
Less resistant to organic solvents
Lighter in weight

## Slide 43: classification of plastics
Thermoplastic soften when heat and harden when cooled Thermosetting materials-shaped permanently.
Groups of laminated pipes
Lower pressure
High pressure

## Slide 44: Fibers
Material obtained from an animal or vegetables
Naturally occurring as polymosis and synthetic metals that can be used to make fibers
Properties of natural fibers:
Elasticity
Has length
Resistant to pressure
Textile fiber products
Flexible

## Slide 45: Wood
Are classified into two:
Soft wood
Hard wood
Properties of wood:
Resist cracking and crutching
They are light compared to other material
Rough until smoothen
Dry up quickly

## Slide 46: Con.,
Have uniform texture
Have good body properties
Uses of wood:
Used in making tables and chairs
Used for making crutches for patients
Used for making walking frame

## Slide 47: Metals
Are classified into two groups
Ferrous – Contains iron steel and steel alloys
Nonferrous- contain carbon and iron
Carbon steel- Sulphur carbon and silicon
General important properties of metals:
Toughness
Corrosive resistance
Malleability- ability to undergo permanent change without breaking

## Slide 48: Cont.,
Tensile strength shears
Comparative strength
Elasticity
Ultimate stress

## Slide 49: Steel Treatment
Heat treatment
Normalizing
Annealing
Tempering

## Slide 50: Types of steel
Surgical steel
Spry steel
Orthopedic steel
Stainless steel
Tool steel

## Slide 51: General characteristics of steel and steel alloys
All have iron and carbon
Examples:
Silicon
Nickel
Double and triple steel
Manganese
Tungsten

## Slide 52: Non Ferrous Metals
Components:
Aluminum
Aluminium alloys
Sources of alluminium:
Cast
Wrought
Copper and copper alloys

## Slide 53: Characteristics of cast alloys
Light
Durable
Characteristics of copper alloys:
Resistance to corrosion
Has attracting finishing
Widely used in electrical work

## Slide 54: Stainless steel
Stainless steel is an alloy of iron and carbon
They are steels that contain at least 10.5% chromium, less than 1.2% carbon
Properties of steel:
Strength- extreme hardness and resistance to wear
Toughness- Does not break easily
Ductility- ability to tolerate being deformed without breaking
weld ability
Durability

## Slide 55: Uses of stainless
Industrial uses such as lock wire and spring wire
Used extensively in the mechanical field due to its ability to meet demanding applications at relatively low cost
Used in kitchen accessories, cutlery and cook ware
Used to make knife blades with sharp edges
Cookers
Grills
Saucepans

## Slide 56: Cont.,
Used in automobile industry

## Slide 57: Tools
Plaster shear- Are large two handled shear used to remove heavy or large plaster casts
Have rounded handles to facilitate ease in cast removal or heavy casts after bone healing following orthopaedic procedures
They are heavy instruments made of premium quality surgical stainless steel
Has a unique design that makes it very distinguishable among different surgical instruments

## Slide 58: Cont.,
The rounded handles allow comfortable essay gripping during manual manipulation
Features two expertly crafted joints and an open jaw incorporating a blade with a reinforced back
This special design allows easy precise and consistent cast removal without injuring adjacent skin
It is notched and rust proof
Made from highest grade stainless steel i.e. 22cm,stainless steel, reusable and fully auto cleavable and measures11.5 inches (29cm)

## Slide 59: Standards of a plaster shear
CE marked
Conforms to medical directive 93/42/EEC
Covered by our lifetime guarantee
Scissors:
These are hand –operated shearing tools
Consist of metal blades pivoted so that the sharpened edges slide against each other when the handles (bows) opposite to the pivot are closed
Used for cutting various thin material such as paper,

## Slide 60: Cont.,
Cardboard, metal foil, cloth, rope and wire
A large variety of scissors exist for specialized purposes
Modern scissors are often designed ergonomically with composite thermoplastic and rubber handles which enable the user to exert either a power grip or a precision grip

## Slide 61: Cont.,
Examples of scissors
Surgical scissors
Hair cutting shears
Blade shearing
Surgical scissors:- are surgical instruments usually used for cutting
- They include :bandage scissors, dissecting scissors, Irish scissors, metzenbaum scissors, plastic surgery scissors and mayo scissors

## Slide 62: Cont.,
Surgical scissors are usually made of very hard material stainless steel for ongoing toughness
Some scissors have tungsten carbide reinforcements along their cutting edges
Its hardness allows the manufactures to create sharper edges which allows for easier and smoother cuts and keeps it sharp for long
Come in different shapes and sizes

## Slide 63: Oscillating machine (plaster saw)
An improved tool which is effective in cutting casts and other hard materials
If the cutter accidentally touches human skin and does not cut fabrics or other objects, it will not cut or damage the skin surface or material unless they are quite strict support
Powered by electricity
Only vibrates with no rotation therefore the skin can withstand contact without being cut

## Slide 64: Plaster spreader (cast spreader)
Strong and durable medical instruments used for plaster and fiberglass casting removal
Made of stainless steel material
Spreads a cut plaster apart after being cut with a plaster cutting tool to enable efficient and safe removal
Uses: when heated and becomes adhesive at body temperature, it is used to:- keep wound edges in position, protects raw surfaces, used to apply drugs to the surface to obtain their systemic effects

## Slide 65: Introducer(T-holder)
Used in orthopaedic surgery
Used to introduce Steinman pin in open surgery procedures
Hammer:
A tool consisting of a weighted head fixed to a long handle that is swung to deliver an impact to a small area of an object

## Slide 66: Cont.,
Examples of uses:
To drill a nail into wood
To shape a metal
To crush a rock
Driving
Shaping
Breaking applications

## Slide 67: Cont.,
The head is made of steel which has been heat treated for hardness
The handle (haft or helve) is typically made wood or plastic
Claw hammer has a claw to pull nails out of wood
Sizes, shapes and structures vary depending on their purposes

## Slide 68: Types of hammers
Sledge hammers
Mallets
Ball peen hammers
Powered hammers
Trip hammers
Note: all the types of hammers are used to deliver forces beyond the capacity of the human arm

## Slide 69: Parts
Head
Handle
Shaft

## Slide 70: Equipment's
Orthopaedic bed: These are beds designed to distribute weight and provide support to the body
They are firmer
They help to improve posture
They are used as part of a healthy back plan care
Components of an ideal orthopaedic bed:
Mechanically operated back rest and knee rest by supper smooth crank mechanism
Epoxy coated mild steel frame work and 4 section perforated top

## Slide 71: Cont.,
Removable high quality head and foot panels
Mounted on protective stumps
Bumper protection of four corners
Types:
Conventional orthopaedic bed- sets are manufactured and designed to avoid putting pressure on any special part of the body
Its intended to offer smooth and even support

## Slide 72: Cont.,
Contoured orthopaedic bed- Made of latex form that will mold to the shape of the body
Primary benefit:
To reduce pain associated with muscular skeletal disorders
To conform to the spine of the user thus reduces strain that occur during sleep
To support the spine
To reduce pressure on patients with joint arthritis

## Slide 73: Walking aids (ambulatory assistive devices)
Are devices designed to assist walking or improve mobility of patients with a mobility impairment
It assists in mobility or transfer within a building or where there are changes of level
Examples of walking aids:
Assistive canes- walking sticks, crutches and walkers
Helps in maintaining an upright ambulation by providing any or of all:

## Slide 74: Cont.,
Improved stability
Reduced lower limb loading
Generates movement
Cane: (walking stick)- simplest type of walking aid held in the hand and tramits load to the floor through the shaft
Crutches: transmits loads to the ground through the shaft
Has two points of contact with the arm, at the hand and either below

## Slide 75: Cont.,
The armpit
Allows significantly greater loads to be exerted through a crutch in comparison with a cane
Forearm crutch: Gives the user support to assist in mobility
helps increase balance, lateral stability and reduces loading on the wrist
Walker (a Zimmer- frame) Most stable walking aid
Consist of a free standing metal frame work with 3 or

## Slide 76: Cont.,
More points of contact which the user places in front of them and grips during movement
Points of contact may either be fixed with rubber ferules, wheels or a combination of both
Wheeled walkers are also known as rollators
They come with an in build seat for the user to rest during use
It has a metal pouch for carrying personal belongings

## Slide 77: Walker cane hybrid
Introduced in 2012
Designed to bridge the gap between a cane and a walker
Has two legs which provide lateral (side to side) support which a cane does not
Can be used with two hands in front of the user, similar to the walker
Provides and increased level of support compared with a cane

## Slide 78: Cont.,
Can be adjusted for use with either one or two hands at the front and at the side, as well as a stair climbing assistant
The hybrid is not designed to replace a walker which normally has four legs and provides 4 way support using both hands
Gait trainers:
More supportive than the standard walker
Typically offer support that assists in weight bearing and balance

## Slide 79: Cont.,
The accessories or product parts that attach to the product provide: unweighting support and postural alignment to enable walking practice

## Slide 80: END
THANK YOU FOR LISTENING