## Slide 1: HEALTH CARE WASTE MANAGEMENT
MD FLORENCE

## Slide 2: Introduction:
Health care waste (HCW) refers to all waste generated in health care facilities such as hospitals, clinics, pharmaceutical manufacturing plants, research laboratories, nursing homes and other settings like homes where there is care for a patient
Health-care waste includes all the wastes generated by medical activities.
These are the waste produced while providing health care and services to the people.
Majority of the health care waste i.e., 75% – 90% are non-risk or general waste. Remaining 10 – 25% of healthcare waste is regarded as hazardous and possess serious threat and health risk.

## Slide 3: CONT…
Every year an estimated 16 billion injections are administered worldwide, but not all of the needles and syringes are properly disposed of afterwards.
Approximately 5.2 million people globally die every year due to diseases caused by improper management of health care waste.
Health care waste management (HCWM) is a process that ensures proper handling and disposal of the HCW in a safe way.
HCWM includes all the steps necessary for waste management from planning to disposal

## Slide 4: Types of Health Care Waste:
1. General Medical Waste:
General medical waste shares large portion in healthcare waste
They are non-hazardous in nature.
General waste includes paper, plastic, and office wastes.
These can be disposed of regularly and don’t require any special handling.

## Slide 5: CONT..
2. Infectious Medical Waste:
Infectious waste can pose several risks of infection to humans, animals, and overall environment.
They contain pathogens.
The waste includes blood-soaked bandages, sharps waste, surgical waste, human or body parts, cultures from laboratory and swabs.
Infectious wastes are treated before disposal and they are to be handled with care.

## Slide 6: CONT…
3. Hazardous Medical Waste:
Hazardous waste is dangerous waste
Sharps fall into this category
Sharps, needles, blades etc. can further puncture the handlers or users
Chemicals, solvents, etc. also fall in this category

## Slide 7: CONT…
4. Radioactive Medical Waste:
These wastes are radioactive in nature.
Waste containing heavy metals, lead, battery, outcomes of radioactive therapies etc. fall in this category
Pathological waste.
Consists of tissues, organs, body parts, human fetuses and animal carcasses, blood, and body fluids. Within this category, recognizable human or animal body parts are also called anatomical waste.
Radioactive medical waste is also considered as a subcategory of infectious waste

## Slide 8: PHARMACEUTICAL WASTE
Expired, unused, and contaminated drugs; vaccines and sera; Pharmaceutical waste includes expired, unused, spilt and contaminated pharmaceutical products, drugs and vaccines.
In this category are also included discarded items used in the handling of pharmaceuticals like bottles, vials, connecting tubing. Since various ministries of health or their equivalents usually put in place specific measures that will reduce the the wastage of drugs, Health care facilities should deal only with small quantities of pharmaceutical wastes.

## Slide 9: Laboratory waste
This is also high risk category waste. This includes chemicals used in the pathological laboratory, microbial cultures and clinical specimens, slide, culture dish, needle, syringes, as well as radioactive waste such as Iodine-125, iodine -131.

## Slide 10: CONT…

## Slide 11: The major sources of health-care waste are:
hospitals and other health-care establishments
laboratories and research centres
mortuary and autopsy centres
animal research and testing laboratories
blood banks and collection services
Nursing homes for the elderly.

## Slide 12: Methods of Health Care Waste Management:

## Slide 13: Incineration:
Incineration is the controlled method of burning the waste
It is one of the oldest and most commonly used method of health care waste management.
In this process, the organic waste is burnt in the high temperature producing mainly gaseous emissions, including steam, carbon dioxide, nitrogen oxides, and certain toxic substances.
The gaseous emissions can be toxic as well.

## Slide 14: CONT..
The incinerator varies from the pit burner to the very sophisticated high temperature running incinerator
Incinerator when operated at optimum temperature kills the pathogen but if it is run at lower temperature, it causes more harm than benefit
Pressurized gas containers, reactive chemical waste, radiographic wastes, waste with high mercury or cadmium content, etc. should never be incinerated

## Slide 15: Chemical disinfection:
Chemical disinfection is used to kill microorganisms on medical equipment, floors and walls
It is also used to the treat the health-care waste.
Chemicals are added to waste to kill or inactivate the pathogens
This method is appropriate for treating liquid waste such as blood, urine, stools, or hospital sewage. However, other waste can also be disinfected using chemical disinfection, before disposal
Anatomical parts, animal carcasses are usually not disinfected.

## Slide 16: Autoclaving:
Autoclaving is an efficient wet thermal disinfection process which is done using an autoclave
Autoclaving is the processes of treatment in pressurized condition.
Reusable medical equipment is sterilized by this process.
An autoclave is used to sterilize reusable medical equipment like surgical equipment, laboratory instruments, pharmaceutical items, and other materials.
This method can be used to sterilize solids, liquids, hollows, and instruments of various shapes and sizes.

## Slide 17: Encapsulation:
In this process, cubic boxes made of high-density polyethylene or metallic drums, are filled with are sharps and chemical or pharmaceutical wastes.
These cubic boxes are not completely filled. The remaining portion is covered with mortar, dried and sealed before disposal.
Encapsulation is very effective in reducing the risk of scavengers or stray animals gaining access to the hazardous health-care waste.
Encapsulation is not suitable for non-sharp infectious waste, but may be used in combination with burning of such waste

## Slide 18: Inertization:
Inertization is the process of mixing waste with cement and other substances before disposal.
This reduces the chance of mixing of toxic substances contained in the waste to surface water or groundwater.
Suitable for pharmaceuticals and for incineration ashes with a high metal.
The typical proportions for the mixture is: 65% pharmaceutical waste, 15% lime, 15% cement and 5% water.
Inertization however is expensive and not suitable for wider variety of waste

## Slide 19: Land disposal:
Land disposal is the way of disposal of waste rather than its treatment.
There are two distinct types of waste disposal to land; open dumps and sanitary landfills.
Open dumps are unmanaged and waste are scattered as well.
The risk of the further transmission of the infection or disease is high.

## Slide 20: CONT…
Sanitary landfills are scientific and designed for the disposal of hazardous waste.
Sanitary landfill prevents contamination of soil and of surface water and groundwater.
Sanitary landfill also checks the air pollution and contact with the public.
Wastes are treated before disposal and managed on daily basis

## Slide 21: Risks Associated with Health Care Waste Management:
Improper health care waste management has negative effects for a everyone.
Those who collect and handle the waste are in more risk along with the general public.
The medical staffs, nurses, the patient, and the children are in high risk.
Waste handlers and the general public who are exposed to HCWM could be at risk of infection with hepatitis A, B and C as sharps and needles can puncture the handlers, if not handled carefully.

## Slide 22: CONT…
Exposure to health care waste can cause diseases like diarrhea, leptospirosis, typhoid, cholera, and HIV, TB etc.
Open burning and incineration of health care wastes can, under some circumstances, result in the emission of dioxins, furans, and particulate matter.
Improper health care waste management pollutes the soil, surface and ground water as well.
Some health care waste management techniques such as incinerator also causes air pollution.

## Slide 23: Risks associated with waste disposal
indirect health risks may occur through the release of toxic pollutants into the environment through treatment or disposal.
Landfills can contaminate drinking-water if they are not properly constructed. Occupational risks exist at disposal facilities that are not well designed, run, or maintained.
Incineration of waste has been widely practised but inadequate incineration or the incineration of unsuitable materials results in the release of pollutants into the air and of ash residue

## Slide 24: Waste management: reasons for failure
Lack of awareness about the health hazards related to health-care waste, inadequate training in proper waste management
absence of waste management and disposal system
, insufficient financial and human resources and the low priority given to the topic are the most common problems connected with health-care waste. Many countries either do not have appropriate regulations, or do not enforce them.
An essential issue is the clear attribution of responsibility for the handling and disposal of waste. According to the 'polluter pays' principle, the responsibility lies with the waste producer, usually the health-care provider, or the establishment involved in related activities. To achieve the safe and sustainable management of health-care waste, financial analyses should include all the costs of disposal.

## Slide 25: Steps towards improvement
Improvements in health-care waste management rely on the following key elements:
building a comprehensive system, addressing responsibilities, resource allocation, handling and disposal. This is a long-term process, sustained by gradual improvements;
raising awareness of the risks related to health-care waste, and of safe and sound practices;

## Slide 26: CONT…
selecting safe and environmentally-friendly management options, to protect people from hazards when collecting, handling, storing, transporting, treating or disposing of waste.
Government commitment and support is needed for universal, long-term improvement, although immediate action can be taken locally.

## Slide 27
END