## Slide 1: CENTRAL NERVOUS SYSTEM IMAGING (LEVEL IV)
DR. N.M KIMANI
LECTURER
DEPT OF DIAGNOSTIC IMAGING

## Slide 2: Central Nervous System
Cranium/Brain
Spine/Spinal cord/Spinal canal

## Slide 3: CENTRAL NERVOUS SYSTEM IMAGING (Neuroimaging, Brain imaging)
Techniques used in either directly or indirectly image the structures, function or pharmacology of the nervous system.
Medicine discipline (neuroscience)
Physicians who specialize in the performance and interpretation of the neuro images are called Neuroradiologists

## Slide 4
Falls into two categories;
1) Structure imaging- deals with structure of nervous system and diagnosis of gross intracranial disease e.g tumors, injury
2) Functional imaging used to diagnose metabolic disease and lesions on a finer scale.
This enables the processing of
information by centers in the
brain to be visualized

## Slide 5: Brain imaging techniques
Plain Radiography (X-RAY)
Computed Tomography(CT)
Magnetic Resonance Imaging (MRI)
-Functional MRI
-MRS (Spectroscopy)
-MR Tractography
Radionuclide Imaging
- Positron Emission Tomography (PET)
- Single Photon Emission Tomography(SPECT)
Cranial Sonography
Event Relate optical signal (EROS)
Diffuse Optical Imaging(DOI)—uses infrared light to generate images of the body

## Slide 6: Plain Radiography (X-RAY)
views
Basic Ap, lateral, townes view.
additional views

## Slide 7: What can we show on x-ray?
FractureS

## Slide 8: .
Assaults ,foreign bodies

## Slide 9
Osteolytic lesions
Metastasis
multiple myeloma
Histiocytosis x

## Slide 10
Sclerotic lesions( bone forming)
Melanotic neuroectodermal tumor of infancy
(MNTI) --rare neoplasms
Hyperostosis frontalis interna
Osteoma in an adult male patient

## Slide 11
Pneumocephalus
Copper beaten appearance

## Slide 12: - Hair-on-end appearance Thalassemia, sickle cell disease

## Slide 13
Advantages
-covers a wide area quickly
- high spatial resolution
- may be used without moving the patient
- available
-low cost

## Slide 14
Disadvantages
radiation
poor resolution
Overlap of structure
Soft tissues not resolved

## Slide 15: Computerised Tomography (CT)
First presented in 1972.
Several generations of scanners. Latest spiral /multislice CT scanner.
3D reconstruction obtained
CT angiography following injection of contrast.
128 slice CT scanner at KNH

## Slide 16: Normal CT scan of the head

## Slide 17
Advantages
Non-invasive
Available
Calcification better defined
Patient easily monitored and even uncooperative patients can be examined
3D reconstruction
NB Minimal requirement in modern neuroradiological unit.
.
Cmv infection

## Slide 18: Computerised tomography
Disadvantages
Artifacts of bone and foreign bodies
Posterior fossa
Isodense lesions may be missed
contrast reactions may occur.

## Slide 19
Facial Bones

## Slide 20: BASE OF SKULL

## Slide 21
3D volume rendered CTA

## Slide 22: Magnetic Resonance Imaging
Has been in use for > 10 years.
Superior to CT especially posterior fossa and lesions of white matter.
Advantages
High tissue contrast
Absence of bone artifacts
Good analysis of anatomical detail in all three planes.

## Slide 23: MRI…contd
Disadvantages
Difficulty visualizing fresh blood
Morphological technique
Long imaging periods. Severe movement artifacts uncooperative patients.
Ferro-magnetic implants e.g. aneurysmal clip contraindicated
Expensive.
Claustrophobia
Noise-due to vibration, patient wears ear defenders
Metallic projectiles-power of magnetic field is substantial metallic objects may cause injury

## Slide 25
sagittal
axial
coronal

## Slide 26: Advances in MRI
MR Spectroscopy-analytical technique used to study metabolic changes in Brain in tumors , infections etc (N- Acetyl Aspartate, Choline, creatinine, lactate, lipids, myo-inositol )
Diffusion Tensor Imaging (DTI)

## Slide 27
MR Tractography

## Slide 28
Functional imaging

## Slide 29: ANGIOGRAPHY
Invasive technique (transfemoral technique)
Usually preceeded by CT or MRI
performed in :-
- subarachnoid haemorrhage
- arterio-venous malformations (AVM)
- pre-operative evaluation of tumour e.g
meningioma.

## Slide 30: Routinely used prior to advent of CT/MRI
Subdural haematoma with midline shift
Extradural haematoma CT

## Slide 31
ANGIOGRAPHY
Now reserved for demonstration of vascular injury
  Dissections
  Ruptures
  Pseudo aneurysms
  Fistulas

## Slide 33: Angio….
INTERVENTIONAL TECHNIQUES
Tumor ablation.
Thrombolysis
Stents
Balloon Angioplasty
Embolization

## Slide 34: Newer angiography techniques
CT/MR Angiography
3D volume rendered CTA

## Slide 35: ULTRASONOGRAPHY
INDICATIONS:
Infant brain
Hydrocephalus/cystic intracranial lesions
Intracranial hemorrhage
Meningitis-monitor progress and complications.
US in-utero;
- anencephaly
-meningocele
-meningomyelocele

## Slide 36: Normal cranial sonograms

## Slide 38: A.Hydranencephaly. B.Aquiductal stenosis. C. Dandy-Walker malfomation
A
B
C

## Slide 39: RADIONUCLIDE IMAGING
Functional information
Poor spatial resolution resulting in limited morphological information.
Capable of identifying region of interest.

## Slide 40: Radionuclide..Contd
1)Positron Emission Tomography(PET)
-Biochemical and functional information.
-Blood volume, blood flow, metabolism
can be studied.
2)Single Photon Emission Tomography
(SPECT)

## Slide 42
Positron Emission Tomography (PET)
traces activity and chemical reactions in the brain and body
PET scan of a normal and healthy Brain
who does not do drugs

## Slide 43
PET Scan

## Slide 44
END END END END